## Slide 1: Metric-Based Cybersecurity Evaluation Methodology for Industrial Embedded Systems
Ángel Longueira Romero
Notes: Hola, buenos días a todos, y gracias por venir. Me llamo Ángel, y voy a contaros el trabajo llevado a cabo durante la tesis titulada «Metodología de evaluación de la ciberseguridad para sistemas embebidos basada en métricas».

## Slide 2: This is me
alongueira@Ikerlan.es
Ángel Longueira Romero
I am Ángel Longueira
I am currently working on my PhD both at IKERLAN in the Cybersecurity Embedded Systems Team, and at MU.
Hello!
Notes: Me llamo Ángel, y estoy hacienda la tesis en el equipo de ciberseguridad en Sistemas Embebidos en IKERLAN, y con el grupo de investigación de análisis de datos y ciberseguridad de la MU, desde marzo del 2019. Antes de entrar en materia, me gustaría dar las gracias a mis directores de tesis, Iñaki Garitano (de la MU) y Rosa Iglesias (de Ikerlan), así como a Jose Luis Flores (de Ikerlan), por su inestimable ayuda.
Grupo de investigación: Análisis de datos y ciberseguridad  Departamento: Electrónica e informática

## Slide 3
1. INTRODUCTION
4. Research Methodology
2. Background
3. Literature Review
5. Contributions
6. Conclusions and future work
Notes: Este va a ser la estructura de la presentación:
Voy a empezar introduciendo el problema que pretendemos resolver con esta tesis
Luego, comentaré los términos clave que son necesarios a lo largo de la presentación
Y después entraremos en materia explicando un poco el estado del arte, y los resultados que obtuvimos
A continuación, comentaré cuáles son las hipótesis que hemos planteado, y cómo pretendemos ponerlas a prueba.
Y finalmente, hablaremos de las contribuciones que hemos hecho, y las conclusiones que hemos extraído, junto con el trabajo futuro.

## Slide 4
Context and Problem
1
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE

## Slide 5: Introduction
EMBEDDED SYSTEMS
DRIVING FORCE OF THE INDUSTRY
THEY PERFORM ALL KINDS OF CRITICAL OPERATIONS
INCREASING COMPLEXITY
REUSE OF OPEN SOURCE AND COTS
GROWING IN NUMBER
INCREASING CONNECTIVITY CAPABILITIES
Notes: Hoy en día, los sistemas embebidos se han convertido en la fuerza motriz detrás del Desarrollo tecnológico que estamos experimentando, con una fuerte presencia en sectores como:
Fabricación,
transporte,
energía,
telecomunicaciones,
salud y
defensa.
Probando ser una pieza clave en la industria cuya importancia va en aumento, ya que normalmente realizan tareas críticas en esos sectores.
Además, sus conectividad va en aumento, tanto entre ellos, como con Internet. Lo que lleva a un aumento en su complejidad.
Por último, también están aumentando rápidamente en número, a ser más fáciles de fabricar, con el uso de elementos OpenSource, y productos de terceros que se pueden integrar directamente en el diseño del sistema embebido.
Este escenario propicia un aumento en el número de amenazas a las que tienen que hacer frente los ES, hacendo que sean un objetivo muy atractivo para los atacantes, por el valor que pueden obtener.

## Slide 6: Introduction
EMBEDDED SYSTEMS
They must be protected
How can we know if an ES is secure enough?
Notes: Entonces, vamos que los Ess son una pieza clave que hay que proteger. Pero, ¿Cómo podemos saber si son seguros? ¿Y cómo podemos hacerlo de una forma repetible, reproducible, y que permita conocer la evolución a lo largo del tiempo?

## Slide 7: Introduction
EVALUATION METHODOLOGY
EVOLUTION OVER TIME
COMPARABLE RESULTS
SOURCE CODE
DESIGN
REPORTING
ORIENTED TO ES
PROCESS
ES
Notes: Durante el planteamiento de esta tesis, vimos que era necesario un proceso que permitiese analizar el propio ES, junto con el diseño o el código fuente. Con la intención de obtener un resultado comparable, que permita hacer un seguimiento del nivel de la ciberseguridad a la largo del tiempo, y acompañado de un informe que especifique cómo se ha llevado a cabo ese proceso.
Ese proceso se corresponde con una metodología de evaluación de la ciberseguridad.

## Slide 8: Introduction
Notes: Si no se le hace ningún tipo de evaluación a un dispositivo, tenderá a ser más inseguro con el descubrimiento de nuevas vulnerabilidades. En cambio, realizando evaluaciones periódicas, que puedan ser comparables, podemos integrar las contramedidas pertinentes en cada caso para que el nivel de ciberseguridad esté dentro de valores aceptables.
Este diagrama es lo que se pretende conseguir con esta tesis: una metodología de evaluación que permita hacer ese seguimiento temporal del estado del dispositivo.

## Slide 9
Background
3
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE
Notes: A continuación, voy a definir los términos clave de esta tesis:

## Slide 10: Background
SYSTEM UNDER TEST (SUT)
Device, software application, or hardware platform that is targeted for a security evaluation.
ASSET
Any component of the SUT that supports information-related activities, including both hardware and software.
WEAKNESS
Flaws, faults, bugs, and other errors in software and hardware design, architecture, code, or implementation that, if left unaddressed, could result in systems, networks, and hardware being vulnerable to attacks.
VULNERABILITY
Flaw in a software, firmware, hardware, or service component resulting from a weakness that can be exploited, causing a negative impact to the confidentiality, integrity, or availability of an impacted component or components.
METRIC
A metric is an indicator resulting from the analysis of the raw data provided by measurement.
Notes: SYSTEM UNDER TEST (SUT)
El sistema bajo test (SUT) se refiere al dispositivo, aplicación software o plataforma hardware que es objetivo de una evaluación de ciberseguridad.
ACTIVO
Es cualquier componente de un SUT que asiste en operaciones relacionadas con información, incluyendo tanto elementos software como hardware.
DEBILIDAD
Es cualquier error, fallo, bug en el diseño, arquitectura o código, tanto SW como HW, que si no es solucionado, podría resultar en potenciales punto de entrada para ataques.
VULNERABILIDAD
Es cualquier error, fallo, bug en el diseño, arquitectura o código, tanto en SW como HW que puede ser explotado para comprometer el sistema.
Todas las vulnerabilidades se apoyan en debilidades, pero no todas las debilidades desembocan en vulnerabilidades.
MÉTRICA
Indicador resultado del análisis de datos obtenidos de medir una propiedad del sistema.

## Slide 11: Background
CVE
Common Vulnerability and Exposure
CPE
Common Platform Enumeration
CWE
Common Weakness Enumeration
CAPEC
Common Attack Pattern Enumeration and Classification
CVSS
Common Vulnerability Scoring System
cpe:2.3:a:microsoft:internet_explorer:8.0.6001:beta:*:*:*:*:*:*
CVE-2022-34488
7.4 HIGH
CWE-119
CAPEC-100
Notes: Por otra parte, también hacemos uso de varios estándares relacionados con la caracterización de activos y vulnerabilidades:
CPE
Identificador único de un Sistema operative, Plataforma hardware o aplicación software.
CVE
Identificador único de una vulnerabilidad
CVSS
Valor de severidad de una vulnerabilidad, en una escala del 0 al 10.
CWE
Identificador único de una debilidad.
CAPEC
Identificador único de un patron de ataque.

## Slide 12
State of the Art
5
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE
Notes: Ahora,voy a comentaros qué hemos hecho en el estado del arte, y qué resultados obtuvimos de esa revisión.

## Slide 13: Literature Review
LITERATURE
Properties
of metrics
Current issues of security metrics
Taxonomies for metrics
Metric analysis
Metrics in the standards
Security Evaluation Methodologies
Aggregation
of metrics
Vulnerability Analysis
Notes: La revisión del estado del arte se puede dividir en dos grandes bloques:
En verde, todo lo relacionado con métricas de ciberseguridad: métricas existentes, propiedades de las métricas, taxonomías, algoritmos de agregación, y problemas detectados.
Y en naranja, todo lo relacionado con metodología de evaluación y análisis de vulnerabilidades: metodologías de evaluación, y técnicas de análisis de vulnerabilidades.
A continuación, voy a explicar cada una de ellas en más detalle, junto con las conclusiones que obtuvimos.

## Slide 14: Results of the Literature Review
More than 500 metrics
Potential application of 150 to ESs
Analysis of Metrics
Metrics in the standards
Properties
of metrics
Taxonomies for metrics
Aggregation
of metrics
Current issues of security metrics
Security Evaluation Methodologies
Vulnerability Analysis
Encourage the use of metrics
EAL in Common Criteria
rav in OSSTMM
Organizational, Technical, and Operational
Usually defined at a very high level (organization, network)
No taxonomy focused on ESs
Lack of the scale, unit and reference values for comparing and interpreting results
Lack of available implementations
Lack of benchmarks for comparison
Included in standards, but no concrete technique is proposed
No evolution over time
Dependency trees and attack graphs, directed graphs
Computer networks
“SMART” and “PRAGMATIC” criteria
Savola identified 19 characteristics (correctness, measurability, meaningfulness)
Lack of consensus and standardization
CVSS does not propose any kind of aggregation mechanism
Three types: Arithmetic Aggregation,
Attack Graph-based Aggregation
Bayesian Network-based Aggregation
Context in not considered
High-level evaluation
High cost and time
Dependence on the evaluator
No comparable results
Notes: ANÁLISIS DE MÉTRICAS
Análisis sistemático de la literatura, usando como referencia las bases de datos del IEEE, ACM, Springer, Google Scholar. Definiendo los términos base a buscar. Las métricas obtenidas de esos artículos fueron filtradas, eliminando aquellas que no eran potencialmente aplicables a ES.
Tasa de intrusiones
Presupuesto dedicado a la ciberseguridad
Número de caminos de ataque
AGREGACIÓN
La mayor parte de los esfuerzos de agregación de la literatura están centrados en agregar valores del CVSS.

## Slide 15
Research Methodology
2
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE
Notes: Con esta visión general del estado del arte, ahora podemos plantear las hipótesis que queremos poner a prueba, qué objetivos tenemos, y cómo pretendemos hacer todo esto.

## Slide 16: Hypothesis
HYPOTHESIS
THE INTRINSIC CHARACTERISTICS OF EMBEDDED SYSTEMS MAKE IT NECESSARY TO CREATE A TAILORED SECURITY EVALUATION METHODOLOGY.
NOT ALL EXISTING SECURITY METRICS PROVIDE A QUANTITATIVE, REPEATABLE AND REPRODUCIBLE VALUE THAT REFLECTS THE SECURITY LEVEL OF THE EMBEDDED SYSTEMS.
THE RESULT OF THE EVALUATION PROCESS SHOULD BE A COMBINATION OF A NUMERIC VALUE AND A DETAILED DESCRIPTION.
BREAKING DOWN THE ES INTO ITS ASSETS MAKES THE SECURITY EVALUATION MORE REPEATABLE.
THE AGGREGATION OF METRICS CAN SERVE TO IDENTIFY THE MORE CRITICAL ELEMENTS IN AN ES, WHILE HELPING TO MAKE DECISIONS ABOUT THE SECURITY STATUS OF THE DEVICE.
PRELIMINAR CONSIDERATIONS

## Slide 17: Objectives
MAIN OBJECTIVE
Design, implementation and validation of an embedded system tailored security evaluation methodology.
EVALUATION METHODOLOGY OBJECTIVE
SECURITY METRICS OBJECTIVE
IDENTIFY THE MAIN DIFFERENCES BETWEEN EVALUATING AN ES AND A TRADITIONAL IT SYSTEM.
IDENTIFY REPEATABLE, REPRODUCIBLE AND QUANTITATIVE SECURITY METRICS, CONSIDERING DIMENSIONS SUCH A MONETARY COST AND TIME.
IDENTIFY AND DEFINE THE SECURITY EVALUATION METHODOLOGY, AND HOW THE SECURITY EVALUATION PROCESS WILL BE DOCUMENTED.
CHECK THE APPLICABILITY OF THE EXISTING SECURITY METRICS, AND THE PROPOSED TAXONOMIES FOR CLASSIFYING THEM.
DEVELOP A MEANINGFUL METHOD FOR METRIC AGGREGATION.
EXPLORE POTENTIAL IMPLICATION OF BREAKING DOWN AN ES INTO ITS BASIC ASSETS.
RE-EVALUATION OVER TIME AND TRACKING.
Notes: El objetivo principal que hemos definido es:
Diseño, implementación y validación de una metodología de evaluación de la seguridad orientada a ES.
Esta tesis tiene dos pilares, el de metodología de evaluación y el de métricas. Y para cada uno de ellos, se han definido objetivos independientes:
Identificar las diferencias entre ES e IT
Identificar las métricas
Identificar y definir la metodología
Comprobar la aplicabilidad de las métricas
Desarrollar el número mínimo de métricas.

## Slide 18
Contributions
4
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE

## Slide 19: Contributions
VULNERABILITY ASSESSMENT
GRAPH-BASED ANALYSIS
SYSTEM UNDER TEST (SUT)
METRICS ANALYSIS
METRIC AGGREGATION
Current Metrics Status
Proposed Taxonomy
Applications
Proposed Model
Proposed Metrics
Model
Algorithm
Notes: Hemos propuesto un proceso de análisis de vulnerabilidades que sigue los siguientes pasos

## Slide 20: Contributions
VULNERABILITY ASSESSMENT
GRAPH-BASED ANALYSIS
SYSTEM UNDER TEST (SUT)
METRICS ANALYSIS
METRIC AGGREGATION
Current Metrics Status
Proposed Taxonomy
Applications
Proposed Model
Proposed Metrics
Model
Algorithm
Notes: Hemos propuesto un proceso de análisis de vulnerabilidades que sigue los siguientes pasos

## Slide 21: Contributions
VULNERABILITY ASSESSMENT
GRAPH-BASED ANALYSIS
SYSTEM UNDER TEST (SUT)
METRICS ANALYSIS
METRIC AGGREGATION
Current Metrics Status
Proposed Taxonomy
Applications
Proposed Model
Proposed Metrics
Model
Algorithm
Notes: Hemos propuesto un proceso de análisis de vulnerabilidades que sigue los siguientes pasos

## Slide 22: Security Metrics Analysis
77.5 % RELATED TO SOFTWARE
0.6 % RELATED TO HARDWARE
14.8 % RELATED TO BOTH
7.1 % RELATED TO OTHERS
SECURITY METRICS
https://embeddedsecuritymetrics.github.io
Analysis
More than 500 metrics
Selection
150 metrics
Testing
20 metrics

## Slide 23: Security Metrics Analysis

## Slide 24: Taxonomy
Elements of the ES that can be evaluated
Which attribute is to be protected (from IEC 62443)
Characteristic parameters
Dashed line indicates AND/OR condition, and solid line AND condition.

## Slide 25: Taxonomy (example)
Test Vector Leakage Assessment (TVLA)
This metric uses statistical tests to measure if a device is prone to a side channel attack by comparing two sets of data: A random one and a fixed one.
Assets: system hardware
Security dimension: data confidentiality
Metric properties
Automation: semi-automation
Scale: nominal (yes/no)
Measurement: dynamic
Computing cost: constant
Notes: hypothesis testing:
welch's t-test concretamente
chi square
DL
Si ese p-value sobrepasa un treshold quiere decir que hay una diferencia estadistica entre ambos conjuntos de datos
el t-test comprueba si las medias de las dos poblaciones distribuidas de forma normal son iguales con X confianza
En SCA se suele usar el treshld de 4.5, que implica un 99,9999% de confianza

## Slide 26: Contributions
VULNERABILITY ASSESSMENT
GRAPH-BASED ANALYSIS
SYSTEM UNDER TEST (SUT)
METRICS ANALYSIS
METRIC AGGREGATION
Current Metrics Status
Proposed Taxonomy
Applications
Proposed Model
Proposed Metrics
Model
Algorithm
Notes: Requiere conocimiento interno del SUT

## Slide 27: Potential applications
VULNERABILITY ASSESSMENT
TRACK THE EVOLUTION OVER TIME
IDENTIFY ROOT CAUSES
EXTRACT NEW REQUIREMENTS
EXTRACT NEW TEST CASES
PROPOSE TRAINING
HELPING IN PATCHING PRIORITIZATION TASKS

## Slide 28: Graph-Based Assessment
CWE
CPE
CVE
CAPEC
CVSS
ROOT NODE
ASSET NODE
VULNERABILITY NODE
NORMAL DEPENDENCY
DEPRECATED DEPENDENCY
Notes: Este modelo necesita tener conocimiento interno del SUT.

## Slide 29: Graph-Based Assessment

## Slide 30: Graph-Based Assessment

## Slide 31: Graph-Based Assessment

## Slide 32: Graph-Based Assessment
VULNERABILITIES
WEAKNESSES
SUT
ASSET
METRICS
Notes: Las métricas dependen del tiempo.

## Slide 33: Graph-Based Assessment
Number of Vulnerabilities Associated to each Weakness for each version of OpenPLC
OpenPLC V1
OpenPLC V2
OpenPLC V3
All Versions

## Slide 34: Contributions
VULNERABILITY ASSESSMENT
GRAPH-BASED ANALYSIS
SYSTEM UNDER TEST (SUT)
METRICS ANALYSIS
METRIC AGGREGATION
Current Metrics Status
Proposed Taxonomy
Applications
Proposed Model
Proposed Metrics
Model
Algorithm
Notes: Hemos propuesto un proceso de análisis de vulnerabilidades que sigue los siguientes pasos

## Slide 35: Metric Aggregation
FUNCTIONALITY FACTOR
DEEPNESS FACTOR
CONTEXT FACTOR
EXPLOIT FACTOR
SUMMARIZED FACTOR
AVERAGE FACTOR
GRAPH-BASED ANALYSIS
AGGREGATION ALGORITHM
Recursive function
Aggregation function
Base case
General case
Bounded
Sensitive
Reality
Notes: Agregamos CVSSs. ¿Por qué se ha elegido el CVSS como métrica de esas 500 iniciales para la agregación?
La fórmula se obtiene de la propuesta en MAGERIT.
Environmental  Exploit (Si se actualizan los valores de las métricas de entorno, el valor es menor que el base)
Temporal  Context (No existe un valor para “aislado”)

## Slide 36: Metric Aggregation
Notes: 9,1. Este valor agregado NO es un CVSS. Se puede interpretar como tal, PERO NO LO ES.

## Slide 37
Publications
4
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE

## Slide 38: Publication Roadmap
2019
2022
Conference paper analyzing existing security metrics, both in standards and in the literature. Proposed taxonomy based on IEC 62443.
Journal paper describing the security evaluation methodology developed. It will include the selected metrics in previous works, and the properties that do not have a metric associated. Comparison with existing methodologies. A method for selecting the right metric will be also proposed.
Conference paper proposing a new aggregation algorithm that takes the real conditions of the SUT into account.
Book chapter expanding the contributions of the thesis.
HOW TO QUANTIFY THE SECURITY LEVEL OF EMBEDDED SYSTEMS? A TAXONOMY OF SECURITY METRICS
A NOVEL MODEL FOR VULNERABILITY ANALYSIS THROUGH ENHANCED DIRECTED GRAPHS AND QUANTITATIVE METRICS
GOTTA CATCH 'EM ALL: AGGREGATING CVSS SCORES
18TH IEEE INTERNATIONAL CONFERENCE ON INDUSTRIAL INFORMATICS
MDPI SENSORS
SPANISH MEETING ON CRYPTOLOGY AND INFORMATION SECURITY (RECSI)
SecDevOps 2023
SECURITY METRICS
VULNERABILITY ANALYSIS
AGGREGATION ALGORITHM
Notes: Ligar cada artículo con su contribución

## Slide 39
Conclusions
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE
4

## Slide 40: Conclusions
EVALUATION METHODOLOGY
SECURITY METRICS
METRIC AGGREGATION
APPLICABILITY OF TAXONOMIES
RELEVANT METRIC IDENTIFICATION
ASSET DECOMPOSITION
RE-EVALUATION OVER TIME
GRAPH-BASED TECHNIQUES
VULNERABILITY ANALYSIS METHODOLOGY
Notes: Hablar también aquí de las hipótesis

## Slide 41: Conclusions
EVALUATION METHODOLOGY
SECURITY METRICS
VULNERABILITY ANALYSIS METHODOLOGY
GRAPH-BASED TECHNIQUES
RE-EVALUATION OVER TIME
ASSET DECOMPOSITION
METRICS FOCUSED ON SW
TESTING EXISTING METRICS
USE IS ENCOURAGE
RELEVANT METRIC IDENTIFICATION
APPLICABILITY OF TAXONOMIES
METRIC AGGREGATION
NO OFFICIAL CVSS AGGREGATION

## Slide 42: Conclusions
TRACK THE EVOLUTION OVER TIME
ANALYZE DEVELOPED DEVICES
ENHANCE THE DEVELOPMENT PROCESS
AUTOMATIC TOOL
PATCHING ACTIVITIES

## Slide 43
Future Work
2
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE

## Slide 44: Future Work
CVSS Update
(submetric)
Integrating humans
in the model
(developers)
Machine Learning Approaches
CONTENT
ANALYZED A REDUCED SET OF METRICS TO TEST THEIR APPLICABILITY TO ESs.
MORE EXTENDED METRICS IN THE INDUSTRY.
DEVELOP A TOOL THAT AUTOMATED THE GENERATION OF EDGS.
INTEGRATE HISTORICAL INFORMATION ABOUT DEVELOPERS.
AGGREGATION AT SUBMETRIC LEVEL.
INTEGRATION OF THE AGGREGATION ALGORITHM WITH THE TOOL OF EDGS.

## Slide 45
Questions
IKERLAN.
WHERE TECHNOLOGY IS AN ATTITUDE
7

## Slide 46: THANK YOU

## Slide 47: Graph-Based Assessment

## Slide 48: Graph-Based Assessment

## Slide 49: Graph-Based Assessment

## Slide 50: Graph-Based Assessment

## Slide 51: Graph-Based Assessment

## Slide 52: Graph-Based Assessment

## Slide 53: Graph-Based Assessment

## Slide 54: Metric Aggregation
Notes: 9,1

## Slide 55: Metric Aggregation

## Slide 56: Metric Aggregation

## Slide 57: Vulnerability Analysis
Vulnerability Assessment
Graph-Based Analysis
System Under Test (SUT)
Metrics Analysis
Track the evolution over time
Identifying root causes
Extracting new requirements
Extracting new test cases
Proposing training
Helping in patching prioritization tasks
Notes: Hemos propuesto un proceso de análisis de vulnerabilidades que sigue los siguientes pasos

## Slide 58: Security Metrics
VULNERABILITY ANALYSIS
METRIC AGGREGATION
METRIC ANALYSIS

## Slide 59: Security Metrics
CONTENT
Properties of Metrics
Current Issues of Security Metrics
Taxonomies for Metrics
Metrics Analysis
Metrics in the Standards
Security Evaluation Methodologies

## Slide 60: Metric Aggregation
Vulnerability Assessment
Graph-Based Analysis
Real Use Case
CONTENT
Aggregation of metrics

## Slide 61: Vulnerability Analysis
Vulnerability Assessment
Graph-Based Analysis
Real Use Case
Metrics Analysis
Security Standards
CONTENT

## Slide 62: Background
Costs
EMBEDDED SYSTEMS
Performance
Power Consumption
Quality and reliability requirements
Memory
Functionality
Operating systems
Scaled-down applications
limited
resources

## Slide 63: Background
LOW-END
EMBEDDED SYSTEMS
HIGH-END
MEDIUM-END
Single core
RAM < 1 MB
CLOCK < tens of MHz
NO OS
One o two cores
1 MB < RAM < 1 GB
Tens of MHz < CLOCK < hundreds of MHz
OS
Multi core
RAM > 1 GB
CLOCK > hundreds of MHz
OS
We will be working here